## Slide 1
Europlexus
User’s Meeting
June 6th 2023
New features and ongoing work
CEA development team
CEA/ISAS/DM2S/SEMT/DYN : C. Gauthier, F. Baj, A. Beccantini, F. Bliard, P. Bouda, S. de Lambert, F. Drui, P. Galon, O. Jamond, N. Lelong

## Slide 2
General information
EPX website : news, documentation, get EPX,…
www-epx.cea.fr
EPX technical support
support-europlexus.cea.fr
EPX licenses
licences-europlexus.cea.fr
EPX environment : Tuleap platform (restricted access for devs and licensed users)
https://codev-tuleap.cea.fr/projects/europlexus
Mailing-list for users
epx-users@saxifrage.saclay.cea.fr
EPX documents library (restricted access)
https://hg2epx.cea.fr

## Slide 3
Outline
Transverse core features
Structural models
FV Pipe models
Explosions
Interfacing EPX
User support
What’s next ?

## Slide 4
Widened compatibilities
  Castem23
  AMR (Adaptivity) + MED
Work on the MPI version
  1D + 2nd order
  FLSX-FV + dynamic domain decomposition
  Widened compatibility of scaled memory (SCLM) option
  New features systematically implemented also in MPI
Work on save/restart
  FLSX-FV (FSI - Immersed boundaries)
  MED
  1D FV elements
Planned :
  AMR + MPI
  VFCC + save/restart + SCLM
Save/restart + MPI
VFCC + VFCC1D
Links
…
Core features
Non-exhaustive list !
ONGOING
DONE

## Slide 5
Cracks visualization by volumetric strain
X damage gradient
Y damage gradient
ENGR - Damage
  DPDC v10 improvement
    Development of a new aggregate interlock model
      Use of the energy dissipated throughout the interface abrasion to extend the initial model to variable opening cracks (avoiding arbitrary hypothesis)
      Good behaviour, robustness of the numerical scheme coupling fracturing and plasticity, but too diffusive damage under extreme loading conditions (restricting cracks opening)
  Phase field method for concrete
    Demonstration of the capability of using an isotropic phase field method with explicit integration without altering time step (ENGR)
      Allows local damage processing (Wu)
      Allows cracks formation (when neighbour energy)
    Development of a new law for ENGR (CUBE) including new distribution and degradation fonctions
      Fits with classical damage laws
      Results independant from characteristic length
Structure models
DONE
DONE

## Slide 6
  Transcription of DPDC (V9 for now) into MFRONT
    MFRONT = constitutive law library interfaced with many softwares
    Code generation
    Implicit integration, Jacobian computed analytically
    Refactoring and performance optimization
    Transposition into other softwares, e.g. MANTA
    In progress : V&V, singularities, viscoplasticity, sensitivity analysis
  Development of a generic phase field model (PhD L. Mersel)
    First implementation and tests in FENICS + MFRONT
Structure models
ONGOING
ONGOING
Zhu test – longitudinal traction, 1MPa
Kalthoff test – Impact on lower crack lip, 16.5 m/s
Notes:       Development of a new aggregate interlock model (exp. basis)
      Use of the energy dissipated throughout the interface abrasion to extend the initial model to variable opening cracks (avoiding arbitrary hypothesis)
      Good behaviour, robustness of the numerical scheme coupling fracturing and plasticity, but too diffusive damage under extreme loading conditions (restricting cracks opening)
    Demonstration of the capability of using an isotropic phase field method with explicit integration without altering time step (ENGR)
      Allows local damage processing (Wu)
      Allows cracks formation (when neighbour energy)
      To do: Integration of the DPDC model and its characteristics (strain rate, friction, aggregate interlock model, plasticity, …)
    Development of a new law for ENGR (CUBE) including new distribution and degradation fonctions
      Fits with classical damage laws
      Results independant from characteristic length

## Slide 7
Displacement on x-axis
Pressure
Development of a dynamic breach model for 1D FV
=> T. Douillet-Grellier / F. Daude talk
BIVF element
MULTiple material : 1 fluid + 1 BREC
Continuity then failure driven by a link
Before failure : BIVF with fluid induced forces on the structure
After failure, 4 options:
  Breach flow computed using 2 different impedances
  Breach flow computed using breach area
  Flow driven by pressure at breacg computed by BRECHE routine
  Flow driven by pressure at breacg computed by BRECHE routine with critical pressure
Failure of a closed loop under pressure
Pipe modeling
DONE

## Slide 8
Numerical and experimental parametric investigation of rarefaction wave propagation across an orifice plate
(PhD F. Bentivegna => see his talk this afternoon)
Application to Loss of Coolant Accident (LOCA) modeling
Tests with different obstacle geometries (serial, multiple holes, …)
Computations with 1D FE fluid elements / comparison with 2D axisymetric computations
Development of impedance models for 1D FV
Pipe modeling
ONGOING

## Slide 9
2nd order in time and space for JWLR multi-component material
Work on « Carbuncle » instability :
  Carbuncle = numerical instabilities around axisymmetric axis with regular fine meshes
  Happens with low-dissipative Riemann solvers
  Strongly reduced with AMR or mapping
  Development of new specific solver(s)
Afterburning model development
Validation
Explosions
Strong reduction of instability with 4 levels of AMR
DONE
ONGOING
ONGOING

## Slide 10
Generic mapping strategy for FV blast computations
  Perform 1D-conic/2D-axisymmeric blast simulation with finite volumes
  Dump a computational state in a mapping file when:
    At some location, the pressure has reached a threshold for the first time
    A specific time is defined
  Initialize a 2D-axisymmeric/3D computation using a (several) mapping file(s) at one (several) location(s)
Explosions
Mapping – EPX vs. Conwep
DONE

## Slide 11
  Work on AMR for FV models :
  Improvements :
    Compatibility MED/AMR
    Compatibility of AMR error indicators in 3D
      INDI : gradient of curvature based refinement
      THRS : min/max threshold
      PCLD FSI : Point-cloud, FSI distance-based criteria
    Compatibility with 3D boundary conditions
  Checks:
    Compatibility with elements
    Compatibility with materials
    Large test case: explosion in a bunker
  Guidelines on how to set AMR parameters for FV computations
Explosion in a bunker – Pressure – Influence of PELE
Explosions
DONE

## Slide 12
Comparison of velocity fields 2D cylindrical piston test case
Comparison of CPU times - 1D cylindrical piston test case
  New low-Mach solver (Cong Huan PHAN PhD thesis):
    New solver based on Artificial Compressibility method (with density correction), available for single phase or two-phase flows
      Efficiency improvement
      Solution accuracy
      Test-cases: Piston (1D & 2D single phase), Bubble expansion (1D two-phase), MARA tests (2D two-phase)
Low-mach solvers
DONE

## Slide 13
Development of a coupling framework :
  EPX as a library
  Integration of an ICoCo interface (initialize, computeTimeStep, fields exchange)
  Python layer for integration into CEA’s generic coupling tool C3PO
Application : coupling neutronics and fluid dynamics to model prompt bursts in molten salt reactors
  Neutronic cross-sections depend on density & temperature
  Power as an energy source term for thermohydraulics
Process applicable to other kinds of models
Apollo3
Europlexus
Power
Density
Temperature
Power.
Pressure
Interfacing EPX
ONGOING

## Slide 14
Development of a framework to use an uncertainties platform with EPX
Instrumentation of EPX test cases and ergonomic use of statistical analysis tools
Uncertainties propagation => Influence of inputs variability on outputs
Sensitivity analysis => relative contribution of inputs
Surrogate models => Build an analytical model from a CPU-costly model (Polynomial, kriging, neural networks)
Example use-cases
Influence of multiple input parameters of DPDC constitutive law
Pipe whip : Build a surrogate model to take into account 3D behavior (plasticity, ovalization) in 1D computations
Interfacing EPX
3D computation of a pipe whip – pressure
ONGOING

## Slide 15
Error messages
  Improvement of error message semantics
  Process :
    Introduction of (102) syntax errors in 6 example data sets browsing a large number of features
    60 unclear messages rewritten
  Long-term work => Don’t hesitate to signal cryptic messages
Formation
  Requested by many users
  Design of training sessions for beginners in progress
  Provide a wide overview of classically-used features (Structure, fluid, FSI)
  First session planned in 2024
Summer 2023 : Reinforced user support
User support
ONGOING
DONE

## Slide 16
What’s next : MANTA
Explicit dynamics for structures and compressible fluids
Fluid / structure interactions
Industrial applications
Finite-elements, finite-volumes, sph, discrete element method
~40 years of development
Generic tool for “implicit problems”
Mainly geared for (non-linear) mechanics
… but also applied to incompressible fluids, electromagnetism, metallurgy, …
Industrial applications
Finite-elements
~40 years of development
Next gen., HPC oriented
Structure / compressible fluids / … , interactions
Industrial applications
Every mesh-based method (FE, FV, HDG, …)
C++
“automatic parallelism”
Easy to maintain and evolve on the long term
Open-source
2030: industrial operation
=> O. Jamond talk

## Slide 17
Thank you !
Any questions ?